Use of the “shape-of-anomaly” data misfit in
3D inversion by planting anomalous densities
Leonardo Uieda
Valéria C. F. Barbosa

---
Difference in shape

---
Scale factor:
{color red d_i} = %alpha {color blue g_i}

---
Scale factor:
{color red d_i} = %alpha {color blue g_i}
SOA = sqrt{sum from i=1 to N {(%alpha {color blue g_i} - {color red d_i})^2}}

---
Scale factor:
{color red d_i} = %alpha {color blue g_i}
SOA = sqrt{sum from i=1 to N {(%alpha {color blue g_i} - {color red d_i})^2}}
%alpha = {sum from i=1 to N {{color blue g_i}{color red d_i}}} over {sum from i=1 to N {{color blue g_i}^2}}
min SOA

---
Predicted (model)
{color red d}, ` {color blue g}
SOA
%alpha
Observed

---
Planting anomalous densities

---
(observed)
color blue g_i

---
mesh

---
(predicted)
color red d_i
seed

---
Choose the best:
%varphi = sqrt{sum from i=1 to N {({color blue g_i} - {color red d_i})^2}}
&
min `of ` %GAMMA = %varphi + %mu %theta
compactness

---
Choose the best:
%varphi = sqrt{sum from i=1 to N {({color blue g_i} - {color red d_i})^2}}
&
min `of ` %GAMMA = SOA + %mu%theta
Exchange for shape-of-anomaly

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
%GAMMA = SOA + %mu %theta
%GAMMA = %varphi + %mu %theta

---
Synthetic tests

---
Redenção granite

---
Bouguer anomaly
Outcrop

---
Bouguer anomaly
Oliveira et al.(2008)
~ 6 km

---
Bouguer anomaly
Oliveira et al.(2008)
Seed at 3km
~ 6 km

---
Known outcrop

---
Known outcrop
Outcrop at wrong place

---
Known outcrop
Outcrop at wrong place
~ 9 km

---
Outcrop at right place

---
Outcrop at right place
~ 6 km

---
5

---
5
6 km

---
In conclusion